## Slide 1: CSC3060 – Computer Architecture Chapter 4 Pipelined Implementation
Prof. Wei Chung Hsu
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Pipelining
Pipelining is an implementation technique in which multiple instructions are overlapped in execution, much like an assembly line.
Single-cycle
Multi-cycle
Pipelined
4 X long cycles
(16 x short cycles)
13 X short cycles
7 X short cycles

## Slide 3: Five Stages of the Simple Data Path
Five stages, one step per stage
IF: Instruction fetch from (instruction) memory
ID: Instruction decode & register read
EX: Execute operation or calculate address
MEM: Access (data) memory operand
WB: Write the result back to register
Initially, this partition is for multi-cycle implementation:
an instruction can finish at stage 3, stage 4 or stage 5

## Slide 4: Divide the Single Cycle Data Path into 5 Stages

## Slide 5: Instruction Timing and Clock Cycle Time
Assume time for a stage is
  100 ps for register to read or write
  200 ps for other stages (Mem and ALU)
Instruction | IF = 200ps | ID=100ps | ALU=200ps | Mem=200ps | WB=100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  | X | 600ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps
Maximum clock frequency for single-cycle implementation= 1/800ps = 1.25 GHz
For multi-cycle implementation, 1/200ps = 5 GHz

## Slide 6: Overlapped Execution in Pipeline
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7 | Cycle 8
LW |  |  |  |  |  |  |  | 
ADD |  |  |  |  |  |  |  | 
BEQ |  |  |  |  |  |  |  | 
SUB |  |  |  |  |  |  |  | 
IF
IF
IF
IF
ID
ID
ID
ID
EXE
EXE
EXE
EXE
MEM
MEM
MEM
MEM
WB
WB
WB
WB
Every instruction takes 5 short cycles
Issue one instruction and retire one instruction per short cycle
Throughput is one instruction per clock cycle
  One instruction per 200ps
  Single cycle implementation will be one instruction per 800ps

## Slide 7: Single cycle, Multi-cycle, Pipelining
Using the table from the previous slides
LW takes 5 clock cycles, Add/sub takes 4 clock cycles, Branch takes 3 cycles, and SW takes 4 cycles
Single-cycle
Multi-cycle
Pipelined
7 X long cycles
(35 short cycles)
5x2 + 4x2 + 3 + 4x2 = 29 short cycles
7 X short cycles + 4 pipe drain = 11 short cycles
Now, for the following code sequence (assuming all instructions are independent)
LW, LW, ADD, SUB, BEQ, SW, SW

## Slide 8: Pipelining Analogy
Four students A, B, C, and D, each have one load of cloth to wash, dray, fold, and put away.
Washer takes 30 minutes
Dryer takes 30 minutes
Folder takes 30 minutes
Stasher takes 30 minutes to put folded cloth into drawer.
Notes: 1. Place one dirty load of clothes in the washer.
2. When the washer is fi nished, place the wet load in the dryer.
3. When the dryer is fi nished, place the dry load on a table and fold.
4. When folding is fi nished, ask your roommate to put the clothes away.

## Slide 9: Sequential Laundry
Notes: 假设每个半小时
1. Place one dirty load of clothes in the washer.
2. When the washer is fi nished, place the wet load in the dryer.
3. When the dryer is fi nished, place the dry load on a table and fold.
4. When folding is fi nished, ask your roommate to put the clothes away.

## Slide 10: Pipelined Laundry
Notes: 假设每个半小时
1. Place one dirty load of clothes in the washer.
2. When the washer is fi nished, place the wet load in the dryer.
3. When the dryer is fi nished, place the dry load on a table and fold.
4. When folding is fi nished, ask your roommate to put the clothes away.

## Slide 11: Pipelined Laundry
Notes: 假设每个半小时
1. Place one dirty load of clothes in the washer.
2. When the washer is fi nished, place the wet load in the dryer.
3. When the dryer is fi nished, place the dry load on a table and fold.
4. When folding is fi nished, ask your roommate to put the clothes away.

## Slide 12: Yale Patt’s Analogy
An African tribe leader wants to have 10 children in one-two years. He calls upon his advisor, who suggests a plan:
Traditional Method (No Pipelining):
  The wife carries a child for 9 months (gestation period).
  This process is repeated 10 times to have 10 children, taking a total of 9 months/child * 10 children = 90 months (7.5 years).
Pipelined Method
  Start conception for child #1
  Begin conception for child #2 after 1 month.
  Repeat this process for all 10 children.
  This process takes 19 months (1.5 year).
This does not work!
The tribe leader is required to have ten wives.

## Slide 14: Single cycle vs. multi-cycle vs. pipeline
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Load
Pipeline
Clk
Single Cycle:
Load
Beq
Waste
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
store
IF
ID
EX
MEM
WB
R-type
Cycle 1
Cycle 2
IF
ID
EX
MEM
WB
Multi-cycle:
IF
ID
EX

## Slide 15: Pipeline Speedup
If all stages are balanced, i.e., all take the same time, in an ideal situation
If not perfectly balanced, speedup would be less
The speedup is a result of increased throughput.
Instruction Latency, which refers to the time it takes for each instruction to be executed, does not decrease; in fact, it may even increase.
Time between instructions pipelined = | Time between instructions nonpipelined
 | Number of pipeline stages

## Slide 16: Pipeline-oriented ISA Design
RISC-V ISA is designed for pipelining
  All instructions are fixed length: 32-bits (except for the C extension)
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Decode and read registers in one step
  Only load/store instructions accessing memory
    Calculate address in the 3rd stage, access memory in the 4th stage
    If the operand is in memory, additional execution stages are needed after stage 4.
  Instructions are simple and do not require a large number of steps

## Slide 17: Pipeline Lessons
Pipeline does not help the latency of a single instruction, but the throughput of the entire program
Pipeline rate is limited by the slowest stage; unbalanced stage length limits the perfect speedup
Multiple tasks are working at the same time using different resources
Potential/Ideal speedup = Number of pipeline stages
Time to “fill” & “drain” the pipeline reduces speedup
  Need to reduce possible fill and drain (e.g., I-cache misses and branch
  misprediction)
Avoid pipeline bubbles from data and control dependencies

## Slide 18: Pipeline Everywhere
Aside from the instruction pipeline, many other areas have implemented pipelined architectures.
  DRAM pipeline
    Row activation, column selection, data transfer
  Cache pipeline
    Address decoding, Way selection, tag match, data retrieval
  Floating point unit pipeline
    Exponent alignment, operation, normalization, rounding, …
  GPU pipeline
    vertex processing, rasterization, fragment processing
  Network pipeline
    packet header processing, routing table lookup, and packet forwarding
If you need to have a higher throughput, think about pipelining.

## Slide 19: Exercise-1
Assume individual stages of the datapath have the following latencies:
Assume that instructions executed by the processor are broken down as follows:
What is the clock time for non-pipeline version and pipeline version ？
1250, 350

## Slide 20: Exercise-1
Assume individual stages of the datapath have the following latencies:
Assume that instructions executed by the processor are broken down as follows:
What is the clock time for non-pipeline version and pipeline version？
What is the latency of an LW instruction in a pipelined and non-pipelined processor?
Non-pipelined: 1250, Pipelined: 1750 (350*5)

## Slide 21: Exercise-1
Assume individual stages of the datapath have the following latencies:
Assume that instructions executed by the processor are broken down as follows:
What is the clock time for non-pipeline version and pipeline version？
What is the latency of an LW instruction in a pipelined and non-pipelined processor?
If we can split a stage, which stage should we split? What is the new cycle time?
1250, 350
1250, 350*5
ID,
MEM 300 ps

## Slide 22: Exercise-1
Assume individual stages of the datapath have the following latencies:
Assume that instructions executed by the processor are broken down as follows:
What is the clock time for non-pipeline version and pipeline version ？
What is the total latency of an LW instruction in a pipelined and non-pipelined processor?
If we can split a stage, which stage should we split? What is the new cycle time?
Compare to multi-cycle implementation, assume lw needs 5 short cycles, ALU needs 4, beq and sw need 3, compute the ideal speedup of Ex(single-cycle/pipeline) and Ex(multi-cycle/pipeline)?
1250, 350
1250, 350*5
ID, 300 ps
1250/350
(0.2*5+0.45*4+0.35*3)
1250/350

## Slide 23: Pipelined RV32I Data Path
t=200ps
The label of each box
indicates its state element
e,g, IMEM, DMEM, Reg
Blue shade means
the element is active
Black shade means
the element is inactive

## Slide 24: What happens Sequentially? Simultaneously?

## Slide 25: Latency vs Throughput
Latency:
Single cycle data path: 800 ps
Pipelined: cycle time=200ps, one instruction takes 5 cycles
200ps x 5 = 1000 ps
Throughput:
Single cycle data path: one instruction every 800 ps
Pipelined: one inst per cycle  one instruction every 200 ps
Pipelined throughput is 4X the single cycle data path method

## Slide 26: What happens to long latency operations?
DIV
Div execution 
Two options:
Stall: the next instruction stalls
at the EXE stage
2) Have a separate long latency
pipeline. Subsequent instructions
can continue to proceed (such as
FP instructions).
Be aware, instructions are typically
retired at the WB stage in order.
So even if the later instructions are
completed sooner than this long
latency operation, they should wait
at the WB stage. This is due to the
possibility of traps.
RISC-V avoids arithmetic exceptions.
So, out-of-order retirement is viable.

## Slide 27: Single Cycle Data Path
Instruction decode:
Generate control signals, No ambiguity
WBsel
ALUop
RegWr
ALUsrc

## Slide 28: Multiple Instructions On-the-Fly in Pipeline
Which immediates to take from?
Which rs1/rs2 to take from?
From instruction at the EXE stage
or instruction from the ID stage?
Which Rd to write?
The Rd from the instruction at the WB stage
or the Rd from the instruction at the ID stage?

## Slide 29: Multiple Instructions On-the-Fly in Pipeline
Which Rd to write?
The Rd from the instruction at the WB stage
or the Rd from the instruction at the ID stage?
ADD t0, t1,t2
SW t0,8(t1)
RegWr
AND t3, t1,t2

## Slide 30: Key to Pipelining: Inserting Pipeline Registers

## Slide 31: Instruction Fetch/Instruction Decode Pipeline Register

## Slide 32: ID/EX Pipeline Register

## Slide 33: EX/MEM Pipeline Register
JAL

## Slide 34: MEM/WB Pipeline Register

## Slide 35: Are Pipelined Registers Architecture States?
No! Pipelined registers are NOT architectural states.
Architecture states
  Registers (general purpose, fp, vector, flags,…)
  PC
  Memory
Micro-architecture states
  Pipelined registers
  Branch predictors
  Caches
  Buffers and Quenes
  Counters
  …
Architecture states are saved during a context switch:
User-level switch, such as a procedure call
Registers are saved on the runtime program stack
2) System-level switch, such as a process switch
Registers are saved on the PCB (Process Control
Block) or the kernel stack.

## Slide 36: Control Signals in Pipelined Data Path
Control signals are derived from instruction bits, that is, after the ID stage.
Control information for later stages are also stored in the pipeline registers