## Slide 1: CSC3060 – Computer Systems FP Numbers and Computation
Prof. Wei Chung Hsu
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: 2.4 Floating-Point Numbers
Representation for non-integral (real) numbers
  Include very small and very large numbers
Like scientific notation (i.e. single digit to the left of the decimal point)
  –2.34 × 1056
  +0.002 × 10–4
In binary, normalized numbers are represented as
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
(normalized: has no leading zeros)
(not normalized)  normalized to 2.0 X 10–7
Int32: max = 4 × 10^9
int64: max ≈ 9 × 10^18
float64: max ≈ 1.8 × 10^308
Example of very large numbers
Number of atoms
Diameter of Milky Way / Universe
Atomic or quantum events
Energy of a supernova
….
Fractional numbers
½, 3.14159, 0.001
1.0e-9
Notes: Real numbers as opposed to “imaginary numbers”
小数点左边只有一位非0数字的，叫做normalized number. 2.0x10–7 = 0.002x10–4
Scientific notation allows the decimal point to float. The Exponent value determines the decimal point.

## Slide 3: 2.4 Floating-Point Numbers
Representation for non-integral (real) numbers
  Include very small and very large numbers
Like scientific notation (i.e. single digit to the left of the decimal point)
  –2.34 × 1056
  +0.002 × 10–4
In binary, normalized numbers are represented as
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
(normalized: has no leading zeros)
(not normalized)  normalized to 2.0 X 10–7
Why normalization?
Unique representation
Maximize precision
Standards
0.00012 x 210
1.02 x 26
Left shift  decrement exp
Right shift  increment exp
Notes: Real numbers as opposed to “imaginary numbers”
小数点左边只有一位非0数字的，叫做normalized number. 2.0x10–7 = 0.002x10–4
Scientific notation allows the decimal point to float. The Exponent value determines the decimal point.

## Slide 4: Number Systems
Decimal numbers
Binary numbers
1000’s column
100’s column
10’s column
1’s column
five
thousands
three
hundreds
seven
tens
four
ones
8’s column
4’s column
2’s column
1’s column
one
eight
one
four
zero
two
one
one
1101.1011
Notes: 10的3次幂： ten to the power of three
乘以： multiply

## Slide 5: FP to Decimal conversion
Convert 1.1011 to decimal
  1 x 20 + 1 x 2-1 + 0 x 2-2 + 1 x 2-3 + 1 x 2-4
  = 1.6875
Convert 0.5 to binary
  0.1
  = 1.0 x 2-1 (normalized)
Convert 0.7 to binary
  0.1011001….
  Getting close to 0.7 (0.6953125..)
0.7 x 2 | 1.4 | 1
0.4 x 2 | 0.8 | 0
0.8 x 2 | 1.6 | 1
0.6 x 2 | 1.2 | 1
0.2 x 2 | 0.4 | 0
0.4 x 2 | 0.8 | 0
0.8 x 2 | 1.6 | 1
How about
0.11111
1.000001
0.11111
= 31/32
1.000001
= 1+1/64

## Slide 6: Floating-Point Standard
Defined by the IEEE 754-1985 standard.
Developed to address inconsistencies in data representation and manipulation.
Portability issues arise for scientific code and data.
Now nearly universally adopted.
Two main representations exist:
  Single precision (32-bit).
  Double precision (64-bit).
  ±1.xxxxxxx2 × 2yyyy

## Slide 7: IEEE Floating-Point Format
s
exponent
fraction/mantissa
1 bit
11 bits
52 bits
x = (−1)s × (1+fraction) × 2(exponent−1023)
s
exponent
fraction/mantissa
1 bit
8 bits
23 bits
x = (−1)s × (1+fraction) × 2(exponent−127)
Single-Precision
Double-Precision
exponent | fraction | Value represented
00000000 | 0 | 0
00000000 | nonzero | denormalized
1111 1111 | 0 | ±∞
1111 1111 | non-zero | NaN
Special values
For denormalized numbers,
there is no hidden 1.
Hidden 1
±1.xxxxxxx2 × 2yyyy
Biased exponent
Notes: IEEE 754 uses a bias of 127 for single precision, double precision的bias是1023

## Slide 8: IEEE Single Precision Floating-Point Numbers
s
exponent
fraction/mantissa
1 bit
8 bits
23 bits
x = (−1)s × (1+fraction) × 2(exponent−127)
Single-Precision
(1+fraction) is called the significand
The largest SP number is (1+0.111111…) x 2(254−127)
which is 2127×(2−ϵ) ~ 3.4028235 × 1038 The bit pattern is 0 11111110 11111111111111111111111
The smallest SP number (normalized) is (1+0.00000…) x 2(1−127)
which is 2-126 The bit pattern is 0 00000001 00000000000000000000000
However, smaller values can be represented using denormalized numbers, where the exponent is 0, and the leading bit of the mantissa is no longer assumed to be 1,
so the smallest number would be 2-149
Notes: IEEE 754 uses a bias of 127 for single precision, double precision的bias是1023

## Slide 9: Exponents in Biased Form
The biased representation simplifies comparisons. We can sort floating-point numbers like integers. A number with a larger exponent will be greater than a number with a smaller exponent (i.e. just call an integer sort routine to sort a group of floating point numbers)
If the exponent is represented in 2’s complement numbers, then a comparison of the exponents must be separated out, not as part of an integer number. Since if treated as part of an integer number, the exponents will be compared like unsigned numbers.
Notes: Real numbers as opposed to “imaginary numbers”
小数点左边只有一位非0数字的，叫做normalized number. 2.0x10–7 = 0.002x10–4
Scientific notation allows the decimal point to float. The Exponent value determines the decimal point.

## Slide 10: Denormalized Numbers
x = (−1)s × (0+fraction) × 2-126
For denormalized numbers, the hidden one is going away
Always -126
x = (−1)s × (0+fraction) × 2(0-127)
WRONG!
Notes: Real numbers as opposed to “imaginary numbers”
小数点左边只有一位非0数字的，叫做normalized number. 2.0x10–7 = 0.002x10–4
Scientific notation allows the decimal point to float. The Exponent value determines the decimal point.

## Slide 11: Why not Fixed-Point Numbers
The range of real numbers we can represent in floating-point numbers is
1038 to 10-38
What if we use a fixed-point representation:
xxxxx.yyyyy where the binary point is fixed.
Assume 32-bit numbers are divided into two parts: the integer part (xxxxx) and the fraction part yyyyy. Each takes 16 bits. What range can this number system cover?
The largest SP number is ~ 3.4028235 × 1038 The bit pattern is 0 11111110 11111111111111111111111
The smallest SP number (normalized) is 2-126 The bit pattern is 0 00000001 00000000000000000000000
Denormalized numbers, where the exponent is 0, and the leading bit of the mantissa is no longer assumed to be 1, the smallest denorm is 2-149

## Slide 12: Why not Fixed-Point Numbers
The range of real numbers we can represent in floating point numbers is
1038 to 10-38
What if we use a fixed point representation:
xxxxx.yyyyy where the binary point is fixed.
Assume 32 bit are divided into two parts: the integer part (xxxxx) and the fraction part yyyyy. Each takes 16 bits. What range can this number system cover?
The largest SP number is ~ 3.4028235 × 1038 The bit pattern is 0 11111110 11111111111111111111111
The smallest SP number (normalized) is 2-126 The bit pattern is 0 00000001 00000000000000000000000
denormalized numbers, where the exponent is 0, and the leading bit of the mantissa is no longer assumed to be 1, the smallest denorm would be 2-149
~215 to ~2-16
~105 to 10-5
Floating point number system can cover a much more extensive range!!
~1038 to 10-38
Notes: Real numbers as opposed to “imaginary numbers”
小数点左边只有一位非0数字的，叫做normalized number. 2.0x10–7 = 0.002x10–4
Scientific notation allows the decimal point to float. The Exponent value determines the decimal point.

## Slide 13: Why does Float cover a Large Range
Both Integer and Float are 32-bit, so why can a float cover such a big range?
The mantissa of a float is 23 bits. It means it can cover integer numbers exactly from 0 to 16,777,216. After this value, the 23 bits of the mantissa no longer hold the precision. So, for example, you can represent 123456789, 123456790, 123456791 in integers, but not in floating point. The numbers around 123456789 can be represented as:
123,456,784 — exactly representable (multiple of 16)
123,456,789 — gets rounded to 123,456,784 in single precision float
123,456,790 — gets rounded to 123,456,784 (same as above)
123,456,791 — also rounded to 123,456,800
Floating-point format is like a telescope with a zoom knob; you can zoom out for a large range or zoom in for very small numbers.

## Slide 14: Why does Float cover a Large Range
Both Integer and Float are 32-bit, so why can a float cover such a big range?
The mantissa of a float is 23 bits. It means it can cover integer numbers exactly from 0 to 16,777,216. After this value, the 23 bits of the mantissa no longer hold the precision. So, for example, you can represent 123456789, 123456790, 123456791 in integers, but not in floating point. The numbers around 123456789 can be represented as:
123,456,784 — exactly representable (multiple of 16)
123,456,789 — gets rounded to 123,456,784 in single precision float
123,456,790 — gets rounded to 123,456,784 (same as above)
123,456,791 — also rounded to 123,456,800
Floating-point format is like a telescope with a zoom knob; you can zoom out for a large range or zoom in for very small numbers.
123456789 in binary is 111010110111100110100010101
To represent it in Single Precision FP is
1.11010110111100110100010101 x
But the fraction part has only 23 bits
1.11010110111100110100010101 x
11010110111100110100010 101
101 has no room to be kept
It must be rounded to 1 in the LSB
So the final representation is
1 10011001 11010110111100110100011
To cover a broader range, you need to sacrifice some precision.

## Slide 15: 2.4.3 Example Numbers
S
e
e
f
f
e
64 patterns, 32 positive, 32 negative
Positive numbers, 4 denormalized
24 normalized, 4 for inf and NaN
1 is 0 011 00
-1 is 1 011 00
How many bit patterns between 1 and -1?
24 bit-patterns
0010xx 1010xx xx means 00 01 10 11
0001xx 1001xx
0000xx 1000xx
6-bit FP format

## Slide 16: Figure 2.35 Bit Patterns from 0 to
8-bit FP format
Denormalized values
Normalized values

## Slide 17: Traditional Supercomputers Are FP Machines
Notes: Binary: [0][100 0000 1][100 0000 0000 0000 0000 0000]
Sign: +
Exponent: 129 – 127 = +2
Mantissa: 0b1.1
x = +0b1.1 x 2^(2) = +0b110 = +6

## Slide 18: Exercise 1
What is the IEEE single precision number 0x40C00000 representing in decimal?
0x40C00000 = 0 100 0000 1 100 0000 0000 0000 0000 0000
= (−1)0 × (1+0.100…000) × 2(129−127)
= 1.100…000 × 22
= 1102
= 6
x = (−1)s × (1+fraction) × 2(exponent−127)
0x40C00000 = 0100 0000 1100 0000 0000 0000 0000 0000
Notes: Binary: [0][100 0000 1][100 0000 0000 0000 0000 0000]
Sign: +
Exponent: 129 – 127 = +2
Mantissa: 0b1.1
x = +0b1.1 x 2^(2) = +0b110 = +6

## Slide 19: Exercise 2
How to represent –0.5 in IEEE single precision binary floating-point format?
–0.5 = (−1)1 × 0.5 (decimal)
= (−1)1 × 1/2 (decimal)
= (−1)1 × 1.0 × 2−1 (binary)
x = (−1)s × (1+fraction) × 2(exponent−127)
1 011 1111 0 000 0000 0000 0000 0000 0000
Notes: 0.5 = 0b0.1 = 0b1 x 2^(-1)
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 20: Exercise 3
How to represent 1/3 in IEEE single precision binary floating-point format?
Notes: 0.5 = 0b0.1 = 0b1 x 2^(-1)
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 21: Exercise 3
How to represent 1/3 in IEEE single precision binary floating-point format?
Multiply by 2, then fetch the integral part
0.3333 x 2 = 0.6666 0
0.6666 x 2 = 1.3332 1
0.3332 x 2 = 0.6664 0
0.6664 x 2 = 1.3328 1
0.3328 x 2 = 0.6656 0
0.6656 x 2 = 1.3312 1
0.010101…. Normalize to 1.0101… x 2−2
Final bit pattern is
0 01111101 01010101010101010101010
x = (−1)s × (1+fraction) × 2(125−127)
Notes: We cannot represent 1/3 exactly, we only get an approximation
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 22: Exercise 4
What are the SP FP values of the following binary numbers
0 00000000 00000000000000000000000
0 00000000 00000000000000000000001
0 00000000 10000000000000000000000
0 00000001 00000000000000000000000
0 10000000 00000000000000000000000
0 01111111 00000000000000000000000
0 11111111 10000000000000000000000
1 11111111 00000000000000000000000
Notes: 0.5 = 0b0.1 = 0b1 x 2^(-1)
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 23: Exercise 4
What are the SP FP values of the following binary numbers
0 00000000 00000000000000000000000
0 00000000 00000000000000000000001
0 00000000 10000000000000000000000
0 00000001 00000000000000000000000
0 10000000 00000000000000000000000
0 01111111 00000000000000000000000
0 11111111 10000000000000000000000
1 11111111 00000000000000000000000
0.0
2-149
2-127
2-126
2.0
1.0
NaN
-∞
For denormalized
values, the exponent
is always set to -126
denom
Notes: 0.0 is neither a normalized nor a denormalized number
Exponent: (-1)+127 = 126 = 0b01111110
Sign = 1
Mantissa: 0000 … 0000
Answer:
1 01111110 000 0000 0000 0000 0000 0000

## Slide 24: 2.4.4 FP Rounding
Floating-point arithmetic can only approximate real arithmetic, since the representation
has a limited range and precision.
Rounding is the task of getting the “closest” matching value x that can be represented in the floating-point format.
IEEE offers 4 rounding modes: Round-to-even, Round-towards 0, Round down, and Round up. The most commonly used (and default) mode is round-to-even.
Round-to-even is also called Round-to-nearest, Ties to even mode.
Round-to-Nearest is easy to understand. What is “ties to even”?
Example:
Value Binary (Fraction) Situation Result (Ties to Even)
12.5 1100.1 Halfway between 12 and 13 12 (Even, 1100)
13.5 1101.1 Halfway between 13 and 14 14 (Even, 1110)

## Slide 25: 2.4.5 FP Operations
Some special rules: 1/−0 is defined to yield −∞, while 1/+0 is defined to yield +∞.
returns NaN
Floating point operations are commutative: (a op b) is the same as (b op a)
FP operation is not associative. For example, with single precision floating point, the expression (3.14+1e10) -1e10 evaluates to 0.0 — the value 3.14 is lost due to rounding. On the other hand, the expression 3.14+(1e10-1e10) evaluates to 3.14.
(a+b)+c is not identical to a+(b+c)
Impact on compiler or programmer:
(A+B+C) (A+(B+C)) (B+A+C) … Can (B+C) be treated as a
CSE (Common Sub-Expression)?
Can (a+b+c+d) be converted to ((a+b) + (c+d))?

## Slide 26: 2.4.5 FP/Int Type Casting
What would happen when casting values to different types?
From int to float, the number cannot overflow, but it may be rounded.
From int or float to double, the exact numeric value can be preserved
Double has both a greater range and a greater precision.
From double to float, the value can overflow to +∞ or −∞, since the range is smaller. Otherwise, it may be rounded, because the precision is smaller.
From float or double to int, the value is rounded toward zero.
For example, 1.999 will be converted to 1, while −1.999 will be converted to −1.
Furthermore, the value may overflow. The C standards do not specify
a fixed result for this case. Intel-compatible microprocessors designate the
bit pattern [10 . . . 00] (TMinw for word size w) as an integer indefinite value.
Any conversion from floating point to integer that cannot assign a reasonable
integer approximation yields this value. Thus, the expression (int) +1e10 yields -21483648,
generating a negative value from a positive one.

## Slide 27: Floating-Point Addition (1)
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 28: Floating-Point Addition (2)
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 29: FP Adder Hardware (1)
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 30: FP Adder Hardware (2)
Step 1
Step 2
Step 3
Step 4

## Slide 31: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP ↔ integer conversion
  (conversion is a relatively expensive operation partly due to the separate FP and Int register files)
Operations usually takes several cycles
  Can be pipelined (the conversion unit may be not)
Notes: reciprocal

## Slide 32: FP Multiply Hardware
FP multiply skips the first step of exponent alignment
They do partial products and add two exponents, two operations in parallel.
Then reduction, normalization, and rounding.
So FP multiply usually takes 4-5 cycles. One cycle longer than FADD.
Reduction

## Slide 33: FMA or FMAC Instructions (1)
Fused Multiply and Add (FMA) or Fused Multiply and Accumulate (FMAC) combines multiply and add in one instruction.
Latency is still 5-6 cycles:
The intermediate product is not rounded before the addition — the addition happens with the full-precision product, and only one rounding is done at the end. So the four steps look like
1. Partial Product Generation
2. Partial Product Reduction
3. Final add together with the last step of reduction
4. Normalization & Rounding
A*B + C

## Slide 34: FMA or FMAC Instructions (2)
FMA (FMAC) offers
  higher throughput (two FLOPs per cycle),
  Lower latency
  higher precision (one rounding instead of two),
  smaller code size, and greater energy efficiency.
Unfortunately, FMA generation is not on by default! You need to turn on some compiler flags:
gcc -O3 -march=native -mfma -ffp-contract=fast
This is because the greater precision may cause the answers generated from FMA to be different from those obtained by separately multiplying and adding – legacy and compatibility issue.

## Slide 35: Quadruple Precision, Half-float and minifloat
Quad-precision float and half float format were defined in IEEE 754-2008.
  Quad precision: 1, 15, 112
  Double precision: 1, 11, 52
  Single precision: 1, 8, 23
  Half precision: 1, 5, 10 (fp16),
    bfloat16 (1,8,7) has the same range as fp32
  Mini-float: 1, 4, 3 (fp8)
  FP4: 1,2,1
  Half-float, mini-float, and fp4, are defined to support AI applications.
Defined by IEEE 754 standard
Starting in Hopper H100 tensor core, in 2022
Starting in Blackwell B100/B200 tensor core, in 2025
Starting in Tesla P100, in 2016
AI/LLM is based on predictions – approximation does not require high precision
Defined by Google, first adopted by TPU, then NVIDIA
Notes: reciprocal

## Slide 36: Quick Review Quiz

## Slide 37: Quick Review
If you are concerned that your integer (data type int) computation may occasionally exceed 4 B (billion), but always < 32 Billion, and want to avoid wrap-around results, what options do you have?
  Use data type long or long long instead of int
  Use double data type instead of int
  Check for integer overflows explicitly to protect from using incorrect data
  Run your programs on 64-bit machines (assuming the LP64 model)
Answer: A, B, C

## Slide 38: Quick Review
2) What are the maximum and minimum values of int32_t?
a) Maximum: , Minimum: −
b) Maximum: 0x7FFFFFFF, Minimum: 0x80000000
c) Maximum: −1 , Minimum: −
d) Maximum: 0x7FFFFFFF, Minimum: 0xFFFFFFFF
Answer: B,C
Notes: A jump instruction may be out of the 1MB range

## Slide 39: Quick Review
3) What is the standard defined for single-precision (SP) and double-precision (DP) floating-point representation and operations?
  IEEE 754-2008
  MXFP standards
  ACM 754-1985
  IEEE 754-1985
Answer: D

## Slide 40: Quick Review
4) What are the maximum and minimum values of a float?
Maximum: ≈3.4× , Minimum: ≈ -3.4×
Maximum: ≈2 × , Minimum: ≈ -2 ×
Maximum: ≈2 × , Minimum: ≈ 1 ×
Maximum: 0x7F7FFFFF, Minimum: 0xFF7FFFFF
Maximum: 0x7F7FFFFF, Minimum: 0x00800000
Answer: A,B,D

## Slide 41: Quick Review
5) What might happen when you cast a double to a float in a C program?
Everything works fine
Loss of precision
Overflow (may set the result to infinity)
Underflow (will be converted to a denormalized value or 0)
Answer: B, C, D

## Slide 42: Quick Review
6) Assume X and Y are integers (int) and A, B, and C are float-point (float) variables. Which of the following expressions are always TRUE?
> 0
(A+B)+C == A + (B+C)
If (X < 0) then –X > 0
X == (int)(float)X;
Answer: None

## Slide 43: Quick Review
7) Which of the following 32-bit patterns are special values in the IEEE 754 single-precision numbers?
0x00000000
0x80000000
0x7F800000
0xFF8FFFFF
Answer: A,B,C,D

## Slide 44: Quick Review
8) IEEE 754-2008 defined half precision fp16 as: 1, 5, 10 format
The range of fp16 (normalized) is
The range of fp16 is
Using fp16 doubles the computational throughput compared to FP32.
Using fp16 reduces the data movements compared to FP32.
Using fp16 reduces the power consumption
Answer: B,C,D,E

## Slide 45: Quick Review
9) Which statements about the FMA instruction are TRUE?
It yields a higher throughput
It yields a lower latency
It increases the computation accuracy
It is the default code generation by the compiler
Answer: A,B,C

## Slide 46: Quick Review
10) Which of the following standards for data representations have been widely adopted?
Two’s complement integers
One’s complement integers
ASCII/Unicode for text and characters
IEEE 754 for floating-point data
ELF for Unix executable and object files
Answer: A,C,D,E